## Slide 1
MD simulation guided different Machine learning models for Predicting the mechanical properties of Ni-Cr based materials
Chandu Cherupally
Merugu Pavan Kalyan
Department of Mechanical Engineering
Machine Learning for materials informatics (MLMI)

## Slide 2
2
Motivation
Computational Expense: MD simulations demand huge computational resources, often taking thousands of CPU hours to model complex alloy systems.
Slow Turnaround Time: Exploring a wide range of alloy compositions is impractical using traditional, serial MD runs — making large-scale screening very slow.
Properties Extraction Challenge: MD provides complex atomic data, but the goal is the macro-scale mechanical properties, which require heavy post-processing to obtain.
Why ML?: ML can learn from past simulation data and quickly capture non-linear relationships between composition, process conditions, and material properties — enabling faster predictions and accelerating the materials discovery process.
Notes: Why you studying this materials

## Slide 3
3
Ni – Cr Alloys (ML + Atomic Simulations))
Ni2Cr Compound
Notes: Why you studying this materials

## Slide 4
Why study Ni-Cr Alloys?
  Ni-Cr alloys (nickel-chromium) are widely used in high-temperature and corrosion-resistant applications.
  Predicting mechanical properties (Young's modulus, yield strength, UTS) accelerates materials design, especially the Ni-Cr Alloys.
  Combining atomistic simulations with ML enables property prediction across composition and conditions.
  This integrated approach helps accelerate alloy design, making the process more data-driven, scalable, and efficient.
4

## Slide 5
Ni-Cr Alloy : Composition and Applications
5

## Slide 6
Young’s Modulus - A measure of stiffness
Properties Predicting
$$E = \frac{\text{Stress}}{\text{Strain}} = \frac{\sigma}{\varepsilon} = \frac{F/A_0}{\Delta L/L_0}$$
Ultimate Tensile Strength – The maximum stress the alloy can withstand before failure
Yield Strength – The stress limit before permanent deformation

## Slide 7
Data Generation Process
Step | Description | Key Components
Model Setup | A virtual Ni-Cr crystal structure is created at the atomic level, defined by an input script that sets the initial temperature and composition. | LAMMPS (Software), Ni-Cr Interatomic Potential (Force Field)
Parameter Sweep | The simulation is repeated across a range of input parameters to build a diverse dataset. These inputs become the features for the ML model. | Composition Ni (at %), Temperature (K), Strain Rate (s(^-1))
Tensile Test | The virtual crystal is stretched by applying a constant strain rate (simulating a high-speed tensile test) while recording the resulting stress. | NPT Ensemble (controls pressure and temperature), Deformation
Raw Data Output | The simulation outputs a time-series log of the system's state, most importantly, the relationship between applied Strain and resulting Stress. | Raw Stress-Strain Curve data (saved in data/raw/)

## Slide 8
Data Generation Process
Stress-Strain Curve
MD Simulation
Processed Properties
(Uts, Youngs Modulus, Yield Strength)
Composition | Temperature (K) | Strain Rate (s^-1)
70% | 300 | 10^8
80% | 600 | 10^9
90% | 900 | 10^9
 |  | 10^10

## Slide 9
Data Extraction and Processing
The raw stress-strain curve data is then analyzed to extract the target mechanical properties
Property Extraction | How It's Taken from the Curve | ML Target Variable
Young's Modulus | Calculated as the slope of the linear (elastic) region of the stress-strain curve. | youngs_modulus
Yield Strength | Determined using the 0.2% offset method on the stress-strain curve. | yield_strength
Ultimate Tensile Strength | The peak stress value (maximum) recorded on the stress-strain curve before the onset of necking/failure. | uts

## Slide 10
Processed Data with properties
Joblib files generated after processing data

## Slide 11
Models training and Evaluation
1. Linear Regression:
2. Ridge Regression:

## Slide 12
3. Random Forest Regressor:
4. MLP Regressor (Neural Networks):
Models training and Evaluation

## Slide 13
ML pipeline

## Slide 14
Results
1. Test Root Mean Squared Error (Test RMSE)
Model | Young's Modulus (Test RMSE) | Yield Strength (Test RMSE) | UTS (Test RMSE)
Linear Regression | 1.15 | 0.035 | 0.028
Ridge Regression | 1.05 | 0.029 | 0.015
Random Forest | 0.75 | 0.021 | 0.020
Neural Network | 1.60 | 0.045 | 0.040
Best Per Property | Random Forest | Random Forest | Ridge Regression

## Slide 15
Results
2. Test R –Squared (Test R^2)
Model | Young's Modulus (Test R²) | Yield Strength (Test R²) | UTS (Test R²)
Linear Regression | 0.825 | 0.790 | 0.810
Ridge Regression | 0.850 | 0.880 | 0.950
Random Forest | 0.920 | 0.935 | 0.930
Neural Network | 0.750 | 0.720 | 0.680
Best Per Property | Random Forest | Random Forest | Ridge Regression

## Slide 16
Plot Results

## Slide 17
Plot Results

## Slide 18
Plot Results

## Slide 19
Plot Results

## Slide 20
Plot Results

## Slide 21
Plot Results

## Slide 22
Plot Results

## Slide 23
Plot Results

## Slide 24
Plot Results

## Slide 25
Plot Results

## Slide 26
Plot Results

## Slide 27
Plot Results

## Slide 28
Model Performances evaluations
Model | Young's Modulus | Yield Strength | UTS | Overall Performance Summary
Random Forest Regressor | Best R^2. Slight overfitting. | Best R^2. Low error. | Very high accuracy. | Highest predictive accuracy (Best for non-linearity).
Ridge Regression | Very stable fit; minimal gap. | Very stable; high accuracy. | Best R^2 / Lowest RMSE. | Most robust and stable generalizer.
Linear Regression (OLS) | Good baseline; low gap. | Solid, reliable accuracy. | Good baseline fit. | Reliable linear performance.
Neural Network (MLP) | Lowest Test $R^2$. | Weakest performance. | Acceptable, but complex. | Acceptable, but requires tuning.

## Slide 29
Models Validations
Validation Type | Purpose | Key Finding
Cross-Validation (5-Fold) | Estimate model stability and variance. | Confirmed Ridge Regression and Linear Regression are highly stable.
Generalization Gap | Detect Overfitting. | All models, except the initial Neural Network, showed strong generalization (low Test error). Random Forest showed a slight, manageable generalization gap.
Baseline Metrics (RAE & R²) | Confirm model utility over simple methods. | All optimized models demonstrated high Test R² (>= 0.8) and RAE <1.0, confirming their predictive utility.

## Slide 30
Conclusions
Machine Learning Effectiveness- ML models successfully predicted the mechanical properties of Ni–Cr alloys — including UTS, Yield Strength, and Young’s Modulus — with strong accuracy..
High Predictive Power - Key properties were successfully predicted with high R^2 values , confirming the model’s utility.
Data Source Validation - Validated that data generated from Molecular Dynamics (MD) simulations is effective and reliable for supervised machine learning tasks.
Best Performer Identified - Random Forest showed the highest overall predictive accuracy and interpretability among the tested models.

## Slide 31
References
Machine Learning Algorithms: Pedregosa, F., et al. (2011), Scikit-learn: Machine Learning in Python, Journal of Machine Learning Research, 12, 2825-2830.
Random Forest Foundation: Breiman, L. (2001). Random Forests. Machine Learning, 45(1), 5-32.
MD Simulation Data Source: MD Simulation Github
Project Github Repo: MLMI_Project